## Slide 1
 | TXC CORPORATION www.txccorp.com |  | 
SPECIFICATION FOR APPROVAL |  |  | 
CUSTOMER PRODUCT TYPE NOMINAL FREQ. TXC P/N REVISION CUSTOMER P/N PM / SALES DATE CUSTOMER CONFIRMATION |  | : : : : : : : : : | ( )
RoHS Compliant |  |  | 
SMD TUNING FORK 3.2X1.5
32.768KHz
9H03200031
A3
(Singnature)
Date
FMT-DOC024 VER.G TXC confidential and proprietary document

## Slide 2
 | TXC CORPORATION www.txccorp.com | 
PRODUCT SPECIFICATION SHEET |  | 
PRODUCT TYPE : SMD TUNING FORK 3.2X1.5 |  | 
NOMINAL FREQ. TXC P/N REVISION |  | 
RoHS Compliant |  | 
PE/RD | QA | MFG
Simon Wang | James Chung | Shu-Chen Ko
2018/6/1 | 2018/6/1 | 2018/6/1
: | 32.768 KHz
: | 9H03200031
: | A3
FMT-DOC024 VER.G TXC confidential and proprietary document

## Slide 3
 | TXC CORPORATION | TXC P/N： 9H03200031 REVISION： A3 PAGE： 1
Rev | Revise page | Revise contents | Date | Ref.No. | Reviser
S1 | N/A | Initial released | 8-Aug-12 | - | Alan Cheng
A1 | N/A | S Turn A | 15-Oct-12 | - | Xiaoyan Jiang
A2 | 3 | Equivalent Series Resistance Change | 15-Jan-15 | EC-O01-150108-01 | Xiaoyan Jiang
A3 | All | Form change ref. DCN-15P030016 TC range: Change from-40~+105 to - 40~+85 | 06/01/18 | EC-O01-180530-01 | Simon Wang
FMT-DOC024 VER.G TXC confidential and proprietary document

## Slide 4
 | TXC CORPORATION | TXC P/N： 9H03200031 REVISION： A3 PAGE： 2
Spec Sheet Contents |  | 
No. | Content | Page
1 | ELECTRICAL SPECIFICATIONS DIMENSIONS SUGGESTED REFLOW PROFILE& MANUAL SOLDER CONDITION | P.3
2 | MARKING PACKING | P.4
3 | PACKING | P.5
4 | STRUCTURE ILLUSTRATION UNIT WEIGHT | P.6
5 | RELIABILITY SPECIFICATIONS | P.7
5 | NOTE | P.8
FMT-DOC024 VER.G TXC confidential and proprietary document

## Slide 5
 |  | TXC CORPORATION |  | TXC P/N： 9H03200031 REVISION： A3 PAGE： 3 |  |  | 
■ ELECTRICAL SPECIFICATIONS |  |  |  |  |  |  | 
■ DIMENSIONS (UNIT:mm) |  |  |  |  |  |  | ■ RECOMMENDED SOLDER PAD (UNIT:mm) 0.65 1.50 ± 0.10 1.70 ± 0.10
1.50 ± 0.10 |  |  |  |  |  |  | 
3.20 ± 0.10 |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 1.8 1.0 1.5 1.0
 |  |  | 0.75 ± 0.10 |  |  |  | 
■ SUGGESTED REFLOW PROFILE ■ TEMPERATURE V.S FREQENCY CURVE |  |  |  |  |  |  | 
Total time : 200 sec. Max. Solder melting point :220℃ |  |  |  |  |  |  | 
(℃) 260 220 180 150 | 10 sec Time (sec) 120 sec |  |  |  |  |  | 
 | Parameters | SYM. | Electrical Spec. |  |  |  | Notes
 |  |  | MIN. | TYP. | MAX. | UNITS | 
1 | Nominal Frequency | F0 | 32.768 |  |  | KHz | -
2 | Frequency Tolerance | - | ± 20 |  |  | ppm | at 25 ℃
3 | Driver Level | DL | - | 0.1 | 1 | uW | -
4 | Load Capacitance | CL | 12.5 |  |  | pF | -
5 | Series Resistance | - | - | - | 65 | Kohms | -
6 | Peak Temperature (Frequency) | - | 20 | 25 | 30 | ℃ | at 25 ℃ ±5℃
7 | Frequency-Temperature coefficent | - | - | - | -0.04 | ppm/℃2 | -
8 | Storage Temperature | - | -55 | ~ | 125 | oC | -
9 | Operating Temperature | - | -40 | ~ | 85 | oC | -
10 | Shunt Capacitance | C0 | - | 1.0 | - | pF | -
11 | Motional Capacitance | C1 | - | 3.4 | - | fF | -
12 | Insulation Resistance | - | 500 | - | - | Mohms | at DC 100V±15V
13 | Aging | - | ±3 |  |  | ppm | 1st Year
-40 25 85 (oC) -130 Δf/fo(ppm)
FMT-DOC024 VER.G TXC confidential and proprietary document
TEMP
60 sec

## Slide 6
 | TXC CORPORATION |  | TXC P/N： 9H03200031 REVISION： A3 PAGE： 4 |  | 
■ MARKING TXC Use Frequency/CL Code Code Date Code TXC Use Date Code This date code will be cycled every four years ■ PACKING |  |  |  |  | 
 |  | Ao= 1.8±0.10 Bo= 3.5±0.10 Ko= 0.87±0.10 |  | mm mm | W1 W
REMARK : 1. 230 mm (9.05) minimum leader which consist of carrier and/or tape followed by a minimum of 160 mm (6.3) of empty carrier tape sealed with cover tape. 2. 160 mm (6.3) minimum trailer of empty carrier tape sealed with cover tape. |  |  |  |  | 
MONTH YEAR |  |  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
2001 | 2005 | 2009 | 2013 | 2017 | A | B | C | D | E | F | G | H | J | K | L | M
2002 | 2006 | 2010 | 2014 | 2018 | N | P | Q | R | S | T | U | V | W | X | Y | Z
2003 | 2007 | 2011 | 2015 | 2019 | a | b | c | d | e | f | g | h | j | k | l | m
2004 | 2008 | 2012 | 2016 | 2020 | n | p | q | r | s | t | u | v | w | x | y | z
CARRIER TAPE DIMENSIONS | K1 | P0 | P1 | P2 | D0 | D1 | E | F | 10P0 | W | T | pcs / Reel
 |  | 4 | 4 | 2 | 1.55 | 1.1 | 1.75 | 5.5 | 40 | 12 | 0.25 | 3K
REEL DIMENSIONS | W | W1 | L | L1
 | 16±1.4 | 13±0.3 | 180+0/-3 | 60.2±0.5
L1
L
KHz | PF | CODE
32.768 | 12.5 | A
FMT-DOC024 VER.G TXC confidential and proprietary document
Frequency /CL
XXXXX
Code

## Slide 7
 | TXC CORPORATION | TXC P/N： 9H03200031 REVISION： A3 PAGE： 5 | 
■ PACKING |  |  | Label B QA Pass
Reel Quantity : 1. Reel X 6 (6 Reels x1 ) H140mm Label B Tape Label A (Label A) Size:100 X 100mm |  |  | 
[STORAGE] 1.The storage time to be 1 year maximum. 2.Don't be caught in the rain. 3.The storage environmentshall be 5℃ ~40℃ temperature and 30% ~ 75%RH humidity and free from the sun shine. 4.If customers have special requirements, we can paste labels according to it. |  |  | 
(Label B) Size:80 X 40mm
FMT-DOC024 VER.G TXC confidential and proprietary document
Box Size:
1. L200 X W200 X
Tape

## Slide 8
 | TXC CORPORATION | TXC P/N： 9H03200031 REVISION： A3 PAGE： 6
■ STRUCTURE ILLUSTRATION |  | 
1 4 6 2 3 |  | 
■ UNIT WEIGHT: 0.01197g/pcs |  | 
NO | COMPONENTS | MATERIALS | FINISH/SPECIFICATIONS
1 | Lid | Kovar(Fe+Co+Ni) Alloy | -
2 | Base(Package) | Ceramic(AI2O3) | Alumina Ceramics
3 | PAD | Au | Tungsten metalize + Ni plating + Au plating
4 | Crystal chip | SiO2 | -
5 | Conductive adhesive | Ag | Silicon resin
6 | Electrode | Au+Cr | -
FMT-DOC024 VER.G TXC confidential and proprietary document
5

## Slide 9
 | TXC CORPORATION | TXC P/N： 9H03200031 REVISION： A3 PAGE： 7
■ RELIABILITY SPECIFICATIONS 1.Mechanical Endurance 2.Environmental Endurance |  | 
No. | Test Item | Test Methods | REF. DOC
2.1 | Resistance To Soldering Heat | Pre-heat temperature Pre-heat time Test temperature Test time | MIL-STD-202
2.2 | High Temp. Storage | + 125 ℃ ± 3 ℃ for 1000 ± 12 hours | MIL-STD-883
2.3 | Low Temp. Storage | - 40 ℃ ± 3 ℃ for 1000 ± 12 hours | MIL-STD-883
2.4 | Thermal Shock | Total 100 cycles of the following temperature cycle 1 cycle 125 ± 3 25 -55 ± 3 10 min. 10 min. max. | MIL-STD-883
2.5 | Pressure Cooker Storage | 121 ± 3℃, RH100%, 2 bar, for 240 hours | EIA-JESD22
2.6 | High Temp＆Humidity | 85℃ ± 3℃ , RH 85% , 1000Hrs | EIA-JESD22
No. | Test Item | Test Methods | REF. DOC
1.1 | Drop Test | 150 cm height, fall freely onto concrete floor 3 times. | MIL-STD-202
1.2 | Mechanical Shock | Device are shocked to half sine wave ( 1000 G ) three mutually perpendicular axes each 3 times. 0.5m sec. duration time | MIL-STD-202
1.3 | Vibration | Frequency range Amplitude Sweep time Perpendicular axes each test time (Total test time 12 hours) | MIL-STD-883
1.4 | Solderability | 245 ℃ ± 5℃ 0.5 mm minimum 5 ± 1 seconds Rosin resin methyl alcohol solvent ( 1 : 4 ) | MIL-STD-883
FMT-DOC024 VER.G TXC confidential and proprietary document
Temperature
Immersing depth Immersion time Flux
10 ~ 2000 Hz
1.52 mm,20G 20 minute
4 hours
125 ℃
60 ~ 120 sec.
260 ± 5 ℃
10 ± 1 sec.
℃
℃
℃
10 min.

## Slide 10
 | TXC CORPORATION | TXC P/N： 9H03200031 REVISION： A3 PAGE： 8
■ SUGGESTED MANUAL SOLDER CONDITION Temperature: 350 ± 10 ℃ Time: 3 sec. Re-solder times: twice ■ FACTORY LOCATION TXC (NINGBO) CORPORATION NO.189 Huang Shan West Road, Beilun District, Ningbo Zhejiang China Measurement condition Electrical characteristics measured by S&A250B or equivalent. NOTE: 1. TXC requires one copy returned with signature and title of authorized individual that signifies acceptance of the attached specifications. 2. Orders received and accepted by TXC after return of signed copy of specification will be produced per these specifications. 3. Any changes to these specifications must be agreed upon by both parties and new revision of the "Product Specification Sheet" will be issued. 4. Any issuance of purchase order prior to consigning back the approval page of "Specification Sheets" from customers will be regarded as the agreement on the contents of these specifications. 5. The green product standard set by TXC is based upon the international standards.Related information is publicly described on the TXC's website, and updated regularly. The document is compliant with the latest green product quality system directives at the time. 6. Revision "Sx" is for engineering samples only. PE/RD's approval required. 7. Revision "Ax" is production ready. PE, QA and MFG's approval required. 8. Inform TXC in advance if you use ultrasonic welding in assembling process . |  | 
FMT-DOC024 VER.G TXC confidential and proprietary document